LXSS Screw Conveyor

Operation Instructions

- Thank you for choosing machines from Jinan Zhuoheng Extrusion Machinery Co., Ltd.

- please read this operation instruction before using the machine

- Welcome to inquiry if anything unclear

Jinan Zhuoheng Extrusion Machinery Co., Ltd

I overview

LXSS Screw Conveyor is one of the special equipment using in extrusion snack food production process to hoist materials. Rely on spiral conveyor positive rotation, convey the powder material or granule material from low to high-end. According to production requirement, hoisting height and throughput needs to custom, solve the problem by manual handling. Saves time and effort, safe and reliable.

II structure of LXSS Screw Conveyor

III Main Technical Data

1 Dimension(L×W×H): 1980mm×600mm×2150mm

2 Power Voltage: 380V

3 motor power: 1.1 kw

4 Output: 150kg/h-200k/h

IV Installation and Maintenance

1 According to the configuration, put LXSS Screw Conveyor on hard and flat ground. Generally, connect Joint hopper of LXSS Screw Conveyor with the outlet of the mixer, while connect the outlet of the LXSS Screw Conveyor with the feeding material hopper of the extruder.

2 Connect the power line of LXSS Screw Conveyor to main power supply control plate correctly.

3 Turn on air switch of LXSS Screw Conveyor, determine the direction of rotation of the spiral conveyor right.

4 In the course of work, don't stretch handle knob to screw material barrel to check or contact material, in order to avoid from personnel injury. When the machine stops working, must clean up it.

5 When operating in strict accordance with the manual operation, and maintenance on time.

Matters need attention

1 when LXSS Screw Conveyor starts to work, please check whether the direction of rotation of the spiral conveyor is right.

2 Cleaning material inside barrel must cut off the power supply firstly, when the machine stop working then start cleaning.

3 In case of power failure and such emergency ,when LXSS Screw Conveyor stops operation, should clean up the material in barrel timely.

4 Regular check the circuit line, prevent from getting an electric shock loose, insulation aging circuit fault.

5 Must pay attention to production safety

The Editor:

Thank you for choose the Jinan Zhuoheng Extrusion Machinery; if you company increase product variety or enlarge the production, our company also have other types of equipments for your select. (reference list). Our company adhering to the "excellent quality, long-last reputation" of the enterprise purpose and "mutual cooperation and common development" business philosophy, Our adhere to the principle of “Sincerity, Innovation and excellence” spirit and dedication, we provide you the good serve and supply on-site installation, commissioning service and free training operators and free offer advanced technology formula and ensure the long-term supply spare parts, the warranty of the machine is for one year free. If there are some problems when need to consult or purchase the spare parts or special order, you can feel free to contact with us, we will meet your requirements as soon as possible.

Thanks again for your using Zhuoheng Extrusion Machinery, Zhuoheng service can bring your convenience and satisfaction, wish have a thriving business and sincerely hope you can propose the ideas and suggestions.