ZR-5A Nitrogen Generation System

Specifications of Each Part of the Equipment as Following

1, Screw Air Compressor

| Items | Content |
| --- | --- |
| Air displacement | 1.6m3/min |
| Working pressure | 0.8Mpa |
| Power | 11KW |
| Oil Content | ≤3ppm |
| Voltage | 380V/3 phases/50HZ |
| Quantity | 1 set |

2, Air Receiver Tank

| Items | Content |
| --- | --- |
| Volume | 600L=0.6m³ |
| Pressure | 1.0Mpa=10Bar |
| Size | 1890*700mm (H*￠) |
| Quantity | 1 piece |

3, ZR-5A Nitrogen Generator (with Air Dryer and Precision Filters)

1) Technical Parameters

| Item | Content |
| --- | --- |
| Nitrogen Capacity | 5Nm³/h |
| Power | 0.9KW |
| Nitrogen Purity | 99.5-99.9% |
| Dew point | ≤-38℃ |
| Air source pressure | 0.8-1.0Mpa |
| Nitrogen Pressure | 0.1-0.65Mpa |
| Weight | 200KG |
| Dimensions | 1100×760×1250mm (L×W×H) |
| Voltage | 220V/1Ph/50HZ |

2) Main Components of the Nitrogen Generator

| NO. | Name | Specifications | Brand | Country |
| --- | --- | --- | --- | --- |
| 1 | Carbon Molecular Sieve | MSC-3KT-172 | JEC | Japan |
| 2 | Magnetic Valve | 4V320-10 | AIRTAC | Taiwan |
| 3 | Controller | DHC-9A | DAHUA | China |
| 4 | Oil-water Separator | AD402-04 | SMC | Japan |
| 5 | Nitrogen Analyzer | Range:79～99.9% | MEICHENG | China |
| 6 | Adsorption Tower | Nonstandard | ZHONGRUI | China |
| 7 | Buffer Tank | Nonstandard | ZHONGRUI | China |
| 8 | Pipe Fitting Rack | Nonstandard | ZHONGRUI | China |

3) Refrigerated Air Dryer & Precision Filters

A. Refrigerated Air Dryer

| Items | Content |
| --- | --- |
| Flow | 1.2m3/min |
| Voltage | 220V/1Ph/50HZ |
| Pressure dew-point | 2-10℃ |
| Quantity | 1 set |

B. Precision Filter

| Items | Content |
| --- | --- |
| Flow | 1.2m3/min |
| Disposal residues | ≤0.01um |
| Residual oil content | ≤0.01ppm |
| Quantity | 3 pieces |

4, Nitrogen Receiver Tank

| Items | Content |
| --- | --- |
| Volume | 300L=0.3m³ |
| Pressure | 0.8Mpa=8Bar |
| Size | 1750*550mm (H*￠) |
| Quantity | 1 piece |