BF600 Flour Mixer

Operation Instructions

- Thank you for choosing machines from Jinan Zhuoheng Extrusion Machinery Co., Ltd.

- please read this operation instruction before using the machine

- Welcome to inquiry if anything unclear

Jinan Zhuoheng Extrusion Machinery Co., Ltd

I overview

BF600 flour mixer is used in snack food production line as raw materials mixing equipment, which is our new research and development of small mixer. The mixing materials barrel adopts deciliter flush mounted, convenient for dismantling cleaning and maintenance. Mixing system uses WPO type reducer drive, large output torque, stable running and stir well, is an ideal material mixing equipment.

II structure of BF600 Flour Mixer

III Main Technical Data

1 Dimension(L×W×H): 900mm×650mm×1100mm

2 Power Voltage: 380V

3 motor power: 4kw

4 Mixing time: 3 minutes-6 minutes

5 Output: 150kg/h-300k/h

IV Installation and Maintenance

1 According to the configuration, put BF600 Flour Mixer

on hard and flat ground.

2 Connect the BF600 Flour Mixer's power line to main power supply control plate

3 Turn on air switch of the BF600 Flour Mixer, determine the direction of rotation of the mixing wings.

4 Check the motor pulley belt tension bridle degree, with tension moderate for good.

5 The machine adopts WPO worm gearbox, when it continuous work for a month, please regularly check whether there is a shortage of oil. If be short of oil, please timely add (20 oil).

6 In the course of work, don't open BF600 Flour Mixer drum cover, and shall not stretch handle knob to mixing material barrel to check or contact material, in order to avoid from personnel injury. When the BF600 Flour Mixer stops working, must clean up it.

7 When operating the BF600 Flour Mixer, should be in strict accordance with the manual operation, and do maintenance on time.

Matters need attention

1 During BF600 Flour Mixer running period, it is strictly prohibited to open the barrel cover and strech hand knob to the barrel.

2 Cleaning material inside barrel must cut off the power supply firstly; when the machine stop working then start cleaning.

3 In case of power failure and such emergency, when mixer stop operation, should clean up the material in barrel timely.

4 Regular check the circuit line, prevent from getting an electric shock loose, insulation aging circuit fault.

5 Must pay attention to production safety.

The Editor:

Thank you for choose the Jinan Zhuoheng Extrusion Machinery; if you company increase product variety or enlarge the production, our company also have other types of equipments for your select. (reference list). Our company adhering to the "excellent quality, long-last reputation" of the enterprise purpose and "mutual cooperation and common development" business philosophy,Our adhere to the principle of “Sincerity, Innovation and excellence” spirit and dedication, we provide you the good serve and supply on-site installation, commissioning service and free training operators and free offer advanced technology formula and ensure the long-term supply spare parts, the warranty of the machine is for one year free. If there are some problems when need to consult or purchase the spare parts or special order, you can feel free to contact with us, we will meet your requirements as soon as possible.