TSJ-G hoists

Operation Instructions

- Thank you for choosing machines from Jinan Zhuoheng Extrusion Machinery Co., Ltd.

- please read this operation instruction before using the machine

- Welcome to inquiry if anything unclear

济南卓恒膨化机械有限公司

JINAN ZHUOHENG EXTRUSION MACHINERYCo.,LTD

1. Overview

TSJ-G hoists are the special equipment to lift and translate material. This equipment runs smoothly, easy to use, and covers an small area, it is the necessary equipment in the production process of the food industry.

- Hoists Structure：

3. Equipment Description:

1. The function

Transfer the raw material from lower position to the higher position.

2. Model explained

TSJ   ----     G

Hoister    High hoist symbol

3. Main technical parameters,

Voltage            three-phase 380V 50Hz

Uses for parts      the power 1.1KW

Dimensions        2280x850x2060mm (Lx w x h)

4. Transport considerations

Screw hoist machine is a mechanical and electrical products, vibration and shock should be avoided during transport phenomena such as sliding collision, overturning, requires the use of appropriate security measures, such as packaging, mounting base, making sure that the device is intact.

5. Installation and commissioning

1, set up the machine on level of solid ground, surrounded by air.

2, the beginning of the power supply should be fitted with a control, a reliable ground connection and zero protection.

3, after fixed location, conduct a comprehensive inspection, if all other parts are intact, and joins loose, ensuring correct rear no-load operation.

4, before running, adjust the hand-wheel positioned bottom; power up, check that if the motor speed is normal, and if the machine is normal.

6. Operation procedures and precautions

1, Check if it is correct of the power supply and the motor turning, power on.

2. Be sure to pay attention to safety, Remember to not reach into breaches.

7. Maintenance

1, check all parts and devices on a regular basis, if identify problems, repairs in timely.

2,clean it after the completion of work, ensure the normal of next use.

3, if the machine keep long periods of inactivity, release the hand-wheel, other parts such as gears, sprockets, should be protected by coating.

4. regularly check the circuit wiring, preventing electric shock loose, insulation aging circuit fault;

5. Pay great attention to production safety!

The Editor:

Thank you for choose the Jinan Zhuoheng Extrusion Machinery; if you company increase product variety or enlarge the production, our company also have other types of equipments for your select. (reference list). Our company adhering to the "excellent quality, long-last reputation" of the enterprise purpose and "mutual cooperation and common development" business philosophy, Our adhere to the principle of “Sincerity, Innovation and excellence” spirit and dedication, we provide you the good serve and supply on-site installation, commissioning service and free training operators and free offer advanced technology formula and ensure the long-term supply spare parts, the warranty of the machine is for one year free. If there are some problems when need to consult or purchase the spare parts or special order, you can feel free to contact with us, we will meet your requirements as soon as possible.

Thanks again for your using Zhuoheng Extrusion Machinery, Zhuoheng service can bring your convenience and satisfaction, wish have a thriving business and sincerely hope you can propose the ideas and suggestions.